## Slide 1
James Kitchens
tskit dev group meeting
August X, 2023
ARG Visualizations with D3.js
https://github.com/kitchensjn/tskit_arg_visualizer

## Slide 2
Current Visualizations
https://tskit.dev/tutorials/viz.html
Viewing the Tree Sequence versus Full ARG
3

## Slide 4
Workflow

## Slide 5
Workflow
Converts tree sequence to JSON object
Using D3.js, creates an SVG from the JSON object
Styling
Displays the SVG either in a Juptyer Notebook or browser

## Slide 6
JSON
https://github.com/kitchensjn/tskit_arg_visualizer/blob/main/plotting.md
Modified versions of the tables from tskit
nodes
links
breakpoints
width
height
tree_highlighting
y_axis
edge_type
subset_nodes
Describes the graph styling

## Slide 7
D3.js Force Directed Graph
https://github.com/d3/d3-force
Node positions are determined by a physics-based simulation:
Nodes repel each other, whereas edges pull connected nodes closer together
Energy of the simulation decreases overtime and nodes come to rest
Nodes’ x and/or y coordinates can be fixed
Nodes are draggable

## Slide 8
How To Run
Jupyter Notebook
Add this header to the top of the notebook:
Terminal
Creates a temporary HTML file and launches in default browser
Jupyter Lab
Add this header to the top of the notebook:

## Slide 11
Ordering of sample nodes is set by the first tree in the tree sequence (these are the only nodes with fixed x-axis positions at the start)
Hoverable blocks corresponding to the different trees in the tree sequence
JSON object is updated as the simulation runs, which means this can be copied, giving user’s the ability to replicate figures
EXPERIMENTAL: a node’s position becomes fixed after dragging, this unfixes the x-axis positions of all nodes except the samples
Three options for the y-axis scale: rank, time, and log_time (all nodes have fixed y-axis positions)

## Slide 13
Three options for the y-axis scale: rank, time, and log_time

## Slide 14
Corresponding recombination nodes have been merged

## Slide 15
With `edge_type=“ortho”`, the visualizer uses the flags of the source and target nodes to set the pathing rules
https://github.com/kitchensjn/tskit_arg_visualizer/blob/main/pathing.md

## Slide 16
Ordering of sample nodes is set by the first tree in the tree sequence (these are the only nodes with fixed x-axis positions at the start)

## Slide 17
All nodes are draggable along the x-axis (nodes have fixed y-axis positions); a node’s position becomes fixed after dragging

## Slide 18
Hoverable blocks corresponding to the different trees in the tree sequence

## Slide 19
EXPERIMENTAL: this unfixes the x-axis positions of all nodes except the samples and allows the simulation to reposition the nodes

## Slide 20
JSON object is updated as the simulation runs, which means this can be copied, giving user’s the ability to replicate figures
Steps to Replicate a Figure
Paste the copied JSON object into a “.json” file and run the following (replacing “example.json” with your file):

## Slide 21
”Simplified” Tree Sequences
Visualizer also works for tree sequences that don’t have marked recombination nodes as long as `edge_type=“line”` (default).
“ortho” edge pathing does not work for that type of tree sequences. All other functionality is the same.

## Slide 22
Best for smaller ARGs
Node positions will still require fine tuning/untangling, particularly around recombination nodes or if the order of the sample nodes isn’t optimal
“ortho” edge pathing can’t yet handle polytomies; `edge_type=“line”` is better for this
Requires a connection to the internet to load D3.js from a CDN
Considerations

## Slide 23
Fix pathing for polytomies
Add a collapsible graph option to better show large ARGs through a subset of nodes
Give ability to easily save the figures to SVG or JPG
Display mutations on edges
Automatically position recombination nodes above there children, if applicable
Stylize line crosses for `edge_type=“line”` as they are for “ortho”
Feature Requests
https://github.com/kitchensjn/tskit_arg_visualizer/issues

## Slide 24
Original ARG
Nodes can be highlighted for collapse
If two neighboring nodes are marked for collapse, they automatically merge.
Collapsed nodes will continue to merge with neighboring nodes that are later marked for collapse.
These nodes are not neighbors and will not merge.